## Slide 1: An Autonomic Control Plane draft-ietf-anima-autonomic-control-plane-05/06
98th IETF, Mar 2017
Michael Behringer (editor), Toerless Eckert, Steinthor Bjarnasson

## Slide 2: Changelog -04 to -05 – grey = detail slides following
Clarifications:
5.3 - ACP neighbor selection: Intent can override only AFTER initial default ACP connection.
5.8.1 - Addressing: ACP addresses permanent, no temporary addresses (RFC4941)
5.2.3 - pointing to GRASP objective defined in I-D.carpenter-anima-ani-objectives
5.9 - routing: prescriptive (aka: mandate RPL) (prior versions was "SHOULD")
6.1 - Connecting non-AN NOC: Eg: introduced term "ACP connect" as name for it.
6.2 - non-ANI-traversal: (from mcr) thoughts on traversing a L3 cloud automated.
10 - Security considerations: No protection inside ACP against source spoofing.
Various formatting changes as supposed by Mcr https://mailarchive.ietf.org/arch/msg/anima/nZpEphrTqDCBdzsKMpaIn2gsIzI
Functional changes:
5.5 - CRL check - Added, open item.
5.8.2 - Addressing: MD5 -> SHA for addr calculation: MD5 obsolete
11. - IANA: Added address sub-scheme assignment (one value)

## Slide 3: New discuss in -05: ACP peer in CRL == certificate became invalid.
Q: OCSP or CRL ?
  Q: Does ACP doc need to make a choice ? Can this be per-device deployment choice or do all devices need to support a common scheme ?
Q: Do we need to support (graceful) recovery ?
  Eg: peer disconnected (ok). But also: Peer “lost” – admin adds it to CRL
  Peer found again in some secure storage. Should be possible to reactivate.
  Current working solution (in ACP spec): factory-reset peer, re-enroll.
  Possible soft recovery (similar to what is done in VPN deployments):
    Intent to ignore CRL entry
    Revoked peer can build ACP
    Intent shows troubled peer that it immediately need to do cert renewal (via ACP)

## Slide 4: Open: Various https://mailarchive.ietf.org/arch/msg/anima/ nZpEphrTqDCBdzsKMpaIn2gsIzI
Most suggestions included in text. Remaining ones:
More explicit text how to deal with admin down interfaces
  A) If possible through implementation locally -> implementation detail
  B) if requiring additional negotation: Extension draft/RFC
  Selection 7 (right place ?): It is desirable to continue being able to run ACP over interfaces that are administratively down or to inquire explicit operator approval upon actions that would administratively bring down an interface and the ACP running across it, especially if bringing down the ACP is known to disconnect the operator from he device
2. Text still claims IPsec/GRE is incompatible with Ipsec (IP/IP)
    Note that without explicit negotiation (eg: via GRASP/TLS), this method is incompatible to direct ACP via IPsec, so it must only be used as an option during GRASP/TLS negotiation.
  Sentence will be removed if one more IPsec expert beside MCR chimes in.
  By default use IKEv2 to negotiate IPsec transport mode with next protocol equal 41 (IPv6).
  If initiator supports and prefers GRE, it should offer GRE (47), it should offer GRE,IPv6.
  Use GRE according to RFC7676 . Set MTU to link level MTU minus IPsec/GRE.
  Application via the ACP need to be built assuming the available MTU is not larger than 1280.

## Slide 5: Open: Various https://mailarchive.ietf.org/arch/msg/anima/ nZpEphrTqDCBdzsKMpaIn2gsIzI
3. Two stage ACP channel security selection – MCR does not like it
  Try supported ACP mechanisms in parallel including GRASP/TLS as one option
  If GRASP/TLS supported, its negotiation result selects channel security
Primary problem example:
  Current target ANIMA device may all like IPsec/IKEv2
  Constrained devices that like CoAP will not have TCP and will have dTLS
  Gateway device (current target ANIMA device) need to support both options
  Current proposed solution supports this.
    Only gateway device needs to support two channel options
    Implementation can be simplified by making CoAP instead of IPsec a per-interface or intent choice – no need to support both channels on same interface!

## Slide 6: Open: Various https://mailarchive.ietf.org/arch/msg/anima/nZpEphrTqDCBdzsKMpaIn2gsIzI
4. 5.5.3. ACP via dTLS So, it's UDP and then... ? GRE inside UDP? (there is a draft tsvwg-gre-in-udp-encap-19)
Goal was to use just IPv6 ACP packets over UDP
  No additional intervening headers
Ask was for constrained devices
  They have CoAP and dTLS code basis
Any reason why this simple solution should not work ?
  UDP port number assignment assumed.
06: Added text to reaffirm that we do not use additional security negotiation such as in eg: OpenConnect VPN or the like.

## Slide 7: Open: Various https://mailarchive.ietf.org/arch/msg/anima/nZpEphrTqDCBdzsKMpaIn2gsIzI
5. 5.5.3. ACP security profile
Several suggestions that would require more/longer work to finalize ?!.
  Eg: there are lot of networks where constrained devices are midpoints in RPL, not only leafs.
Consideration:
  Existing text for “constrained devices” == like to do dTLS is an attempt to show how to modify ANIMA for a specific device class
  If this approach MAY ME incomplete and require follow-on work, suggest to leave it in and do that work in followup draft when desired.
  If this approach is so far off that it is more confusing, let’s remove all “constrained devices” text from ACP doc
  If the thoughts are useful… move to appendix/summarize there as incomplete..

## Slide 8: 5.9 Open EDNOTE: RPL parameters / profile Need to decide: storing / non-storing mode; mcr suggests storing mode. Need to define more parameters in detail
Text added to 06. MCR suggesting to translaet into standard RPL profile definition in -07
Suggestion from Pascal Thubert / Toerless:
  RPL Mode of Operations (MOP): mode 3 “Storing Mode of Operations with multicast support”. Implementations should support also other modes. Note: Root indicates mode in DIO flow.
  Objective Function (OF): Use OF0 [RFC6552]. No use of metric containers, Default RPLInstanceID = 0.
    stretch_rank: none provided (“not stretched”).
    rank_factor: Derived from link speed: <= 100Mbps: LOW_SPEED_FACTOR(5), else HIGH_SPEED_FACTOR(1)
  Trickle: Not used; Data Path Validation: Not used
  Proactive, aggressive DAO state maintenance:
    Use K-flag in unsolicited DAO indicating change from previous information (to require DAO-ACK). Retry such DAO DAO-RETRIES(3) times with DAO-ACK_TIME_OUT(256ms) in between.
  Administrative Preference (RFC6550, 3.2.6 – to become root) (toerless):
    Indicated in DODAGPreference field of DIO message.
    Explicit configured ”root” registrar: 0b100; Registrar (Default): 0b011; AN-connect (non registrar): 0b010; Default: 0b001.
Extensibility:
  RPL/Root (direct or via intent) may create additional RPL instances with other OF/metrics.

## Slide 9: Old discuss from -03 (Berlin) 5.1.1 – Format of domain Certificate with ANIMA information https://mailarchive.ietf.org/arch/msg/anima/nTgDaP4_-TKbQShmfb_BWu8kFp8
Text is in ACP draft (not bootstrap draft) because
  No ACP specific text in bootstrap -> easier to reuse in non ANIMA solutions
  Easier to read ACP (without having to follow references)
  Thought this was agreed with bootstrap team ?!
B) (strange but “clever”?!) formatting choosen because…
  Example: anima.acp+<acp-addr>@<acp-domain> subjectAltname RFC822format
  Existing subjectAlname type = works with any (badly implemented) ASN.1 parser
  Tagged: “anima.acp” – immediately possible to distinguish from other subjectAltnames
  RFC822format allows to carry both <addr> AND <acp-domain> in one subjectAltname
  Even if address is mistaken by some system, worst case an email gets sent to address
    And ACP administrator could catch those -> set up email anima.acp@<acp-domain>
    RFC822 mailbox behavior: extensions after + are part of preceding mailbox name.
  06: added more detailed version of above explanations.

## Slide 10: Candidate TBD
Do we like document structure:
  I-D.carpenter-anima-ani-objectives to be a dependency of ACP and other drafts ?
    If we move ACP objectives into ACP draft, appropriate to add co-authors ?
TODO: Merge text into ACP text
  Section 5.2.3
  See BRSKY draft 3.1.1 to compare

## Slide 11: 11 – security considerations, source spoofing
If malicious device get access to ACP -> spoofing possible
  Sounds bad, but its not…
Intentionally no further protection to keep solution lightweight:
  Hop-by-hop ACP security as first layer of protection for protocols running inside of it (GRASP, RPL, any “user/operator” protocols: NTP, SNMP, DNS, …)
This is not worse than todays IGP routing (even with security)
  For bidirectional traffic you need to also spoof routes or be near the root
  Spoofing routes as difficult as hacking IGP with (cert) security
Full Solution: ACP-cert authenticated RPL messages (transitive)
  Eg: Similar to BGP… Never done intradomain... ETOOMUCHTROUBLE ?!
How to best state this in security section ?!

## Slide 12: Next steps
Close what we can in Chicago
Candidate last call version before next IETF.